Lab 6 Questions

1) There are two bugs
2) One of the bugs is that in line 14 and 15, the immediate should be 4 because all the addresses are offest by 4. The other is that the loop is going one too far, so a line should be added after the next element is loaded to check whether it is 0, and if it is the loop will break.
3) To find the bugs I stepped through the program to try and figure out why the loop was going too far.
4) source is stored in $9
5) dest is stored in $10
6) The pointers are loaded in line 28, “la $9, source” and line 33, “la $10, dest”
7) Line 34, $L6
8)	Instruction: addu $8, $8, 1
Purpose: Adds one to the value in $8
Corresponding C: x = x + 1

Instruction: sll $3, $8, 2
Purpose: Moves the bits in $8 to the left by two, which multiplies it by 4, and stores that number in	$3.
Corresponding C:

Instruction: addu $5, $7, $9
Purpose: Adds $7 and $9 and stores it in $5
Corresponding C: x = y + z

Instruction: addu $2, $3, $9
Purpose: Adds $3 and $9 and stores it in $2
Corresponding C: x = y + z

Instruction: addu $6, $7, $10
Purpose: Adds $7 and $10 and stores it in $6
Corresponding C: x = y + z

Instruction: lw $4, 0($2)
Purpose: Loads the value of $2 into $4
Corresponding C: x = y (where x is $4 and y is $2)

Instruction: move $7, $3
Purpose: Copies the value in $3 to $7
Corresponding C: x = y (where x is $7 and y is $3)

Instruction: lw $3, 0($5)
Purpose: Loads the value of $5 into $3
Corresponding C: x = y (where x is $3 and y is $5)

Instruction: sw $3, 0($6)
Purpose: Stores the value of $3 into $6
Corresponding C: x = y (where x is $6 and y is $3)

Instruction: bne $4, $0, $L6
Purpose: Jumps to label $L6 if the value in $4 is not equal to 0
Corresponding C: The loop at $L6 is similar to a while loop that only runs while the next number
is not 0.